## Slide 1: SMART HOPPING® 2.0 Access Point 2.4GHz (RTX3471)

## Slide 2: Learning objectives
Upon successful completion of the course the learner will be able to
  Discuss the features and benefits of the new SMART HOPPING® 2.0 Access Point
  Identify system compatibility
  Understand the technical similarities and differences between the SMART HOPPING® 2.0 Access Point and the existing SMART HOPPING® 1.0 Access Points
  Understand the mounting options available for the SMART HOPPING® 2.0 Access Point, and how to order to them
  Troubleshoot the SMART HOPPING® 2.0 Access Point
  Operate the new Upgrader Tool

## Slide 3: Chapter/Module objectives
This chapter/module will cover the following topics
Overview
Compatibility
Documentation
Products and ordering
Comparison
  Basic installation
  Layer 3 installation
Troubleshooting
Test and inspection

## Slide 4: Overview
Infrastructure
First release
Plan for future releases
Design
Mounting alternatives
Size comparison

## Slide 5: Introducing RTX3471 – SMART HOPPING® 2.0 Access Point 2.4 GHz
The SMART HOPPING® 2.0 infrastructure will be the foundation for SMART HOPPING® wireless communication in the future.
After 19 years of successful SMART HOPPING® 1.0 deployments, market-leading SMART HOPPING® technology is evolving to help meet the needs of our customers into the future, starting with a new Access Point. The new access point can function in existing SMART HOPPING® 1.0 networks today and will be upgradeable in the future (software upgrade) to provide increased bandwidth over the wireless link and increased network security.
The release of SMART HOPPING® 2.0, Access Point 2.4GHz is aimed for Worldwide Markets. Except USA and Puerto Rico.

## Slide 6: SMART HOPPING® 2.0 Access Point 2.4GHz release
The new SMART HOPPING® 2.0 Access Point can function in existing SMART HOPPING® 1.0 networks today with performance equivalent to the SMART HOPPING® 1.0 system. In the future, the SMART HOPPING® 2.0 Access Point software will be upgradeable to provide SMART HOPPING® 2.0 functionality (increased bandwidth over the wireless link and increased network security).
Access Point Controller
2.4 GHz Access Point
SH 2.0 AP HW
SW: SH 1.0 Operation
First release
SH: SMART HOPPING®, AP: Access Point, APC: Access Point Controller, SW: Software, HW: Hardware, RA: Revision A

## Slide 7: Overview: Plan for SMART HOPPING® 2.0 future releases
Following the 2.4 GHz Access Point release, the current plan is to release new Access Point Controller software that initially will only be available for installation as a virtual Access Point Controller.
Included in this release will be new software for the SMART HOPPING® 2.0 access point to enable SMART HOPPING® 2.0 features.
Access Point Controller
2.4 GHz Access Point
Virtual APC
SH 2.0 APC SW
SH 2.0 AP HW
SW: SH 1.0 Operation
SW: Add SH 2.0 Operation
Future
First release
SH: SMART HOPPING®, AP: Access Point, APC: Access Point Controller, SW: Software, HW: Hardware, RA: Revision A

## Slide 8: Overview: Plan for SMART HOPPING® 2.0 future releases
The next planned release will be for a hardware replacement of the existing Access Point Controller.
Access Point Controller
2.4 GHz Access Point
Virtual APC
SH 2.0 APC SW
SH 2.0 APC HW
SH 2.0 APC SW
SH 2.0 AP HW
SW: SH 1.0 Operation
SW: Add SH 2.0 Operation
Future
Future
First release
SH: SMART HOPPING®, AP: Access Point, APC: Access Point Controller, SW: Software, HW: Hardware, RA: Revision A

## Slide 9: Introducing: RTX3471 – SMART HOPPING® 2.0 Access Point 2.4GHz
The SMART HOPPING® 2.0 Access Point has been designed to eliminate the antenna whips (aerials).
Although the physical design and mounting of the SMART HOPPING® 2.0 Access Point are different from the SMART HOPPING® 1.0 Access Point, the radio frequency performance of the SMART HOPPING® 2.0 Access Point allows the Access Point to be placed in the same location as an existing SMART HOPPING® 1.0 Access Point with performance equivalent to the SMART HOPPING® 1.0 system.

## Slide 10: SMART HOPPING® 2.0 Access Point mounting alternatives
Wall mount
Wall mount with cosmetic cover
Below ceiling mount
Below ceiling mount with cosmetic cover
Flush ceiling mount
Technology solutions: Oberon enclosure

## Slide 11: SMART HOPPING® 2.0 Access Point size comparison
1.2 x 8.0 x 9.6 inches
77 square inches
1.2 x 6.4 x 6.4 inches
41.0 square inches
47% smaller!
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
6.3 inches Antenna Whip (Aerial)

## Slide 12: Exercise/Exam
Question
Answer

## Slide 13: Question 1
Which of the following statements apply to the RTX3471 - Philips SMART HOPPING® 2.0 Access Point 2.4GHz?
The access point software will be upgradeable in the future to provide increased bandwidth over the wireless link and increased network security.
The access point may be placed in the same location as an existing SMART HOPPING® 1.0 Access Point with performance equivalent to the SMART HOPPING® 1.0 system.
The access point does not have external antenna whips – it uses internal antennas.
All of the above.

## Slide 14: Question 1
Which of the following statements apply to the RTX3471 - SMART HOPPING® 2.0 Access Point 2.4 GHz?
The access point software will be upgradeable in the future to provide increased bandwidth over the wireless link and increased network security.
The access point may be placed in the same location as an existing SMART HOPPING® 1.0 Access Point with performance equivalent to the SMART HOPPING® 1.0 system.
The access point does not have external antenna whips – it uses internal antennas.
All of the above.
Answer 1:
d – All of the statements above apply to the RTX3471 - SMART HOPPING® 2.0 Access Point 2.4 GHz

## Slide 15: Compatibility
Software compatibility and reporting revisions
SMART HOPPING® 1.0 to SMART HOPPING® 2.0 migration guidance

## Slide 16: Compatibility
The new SMART HOPPING® 2.0 Access Point can function in existing SMART HOPPING® 1.0 networks today with performance equivalent to the SMART HOPPING® 1.0 system.
Although the physical design and mounting of the SMART HOPPING® 2.0 Access Point are different from the SMART HOPPING® 1.0 Access Point, the radio frequency performance of the SMART HOPPING® 2.0 Access Point allows the Access Point to be placed in the same location as an existing SMART HOPPING® 1.0 Access Point with performance equivalent to the SMART HOPPING® 1.0 system.
In the future, the SMART HOPPING® 2.0 Access Point the software will be upgradeable to provide SMART HOPPING® 2.0 functionality (increased bandwidth over the wireless link and increased network security).
Generation 1 (Gen 1) and Generation 2 (Gen 2) SMART HOPPING® 1.0 Access Points will not support future SMART HOPPING® 2.0 wireless clients.
Gen 1 2.4 GHz Access Points = >
    part number: 862232
Gen 2 2.4 GHz Access Points = >
    part number: 94100009
Circa: 2004-2007
Revision reported: B.00.12
Circa: 2007-2011
Revision reported: C.00.07 or D.01.22

## Slide 17: Software compatibility and reporting revisions
For SMART HOPPING® 2.0 we have changed to the Philips standard software revision scheme – for example 6.0.00.06 or F.00.06. So how will an Access Point that uses this new standard appear in SMART HOPPING® applications that use V.UU.FF (e.g. D.02.23 Access Point Controller)?
Where: 1 = A
2 = B
3 = C
4 = D
5 = E (Used in SMART HOPPING® 1.0)
6 = F (Used in SMART HOPPING® 2.0)
New
V.UU.FF
6 . 00 . 06
F . 00 . 06

## Slide 18: Software compatibility and reporting revisions
For SMART HOPPING® 2.0 we have changed to the Philips standard software revision scheme – for example 6.0.3.0 or F.0.3.0. So how will an Access Point that uses this new standard appear in SMART HOPPING® applications that use V.UU.FF (e.g. D.02.23 Access Point Controller)?
Access Point Controller web browser interface
Upgrader user interface
Where: 1 = A
2 = B
3 = C
4 = D
5 = E
6 = F
New
V.UU.FF
6 . 00 . 06
F . 00 . 06

## Slide 19: Software compatibility table for 2.4 GHz Layer 2 SMART HOPPING® deployments
Compatibility Tables:
New products and software are shown in dark blue background and white text.
Older, supported versions of software are shown in light blue background with black text.
Supported systems are outlined in dark blue.

## Slide 20: Software compatibility table for 2.4 GHz Layer 3 SMART HOPPING® deployments
Compatibility Tables:
New products and software are shown in dark blue background and white text.
Older, supported versions of software are shown in light blue background with black text.
Supported systems are outlined in dark blue.

## Slide 21: SMART HOPPING® 1.0 to SMART HOPPING® 2.0 migration guidance
To determine what devices are present in the existing system, if the Access Point Controller are >= D.01.01, the SMART HOPPING® 2.0 Upgrader Tool can be used to export a .csv file with details on the equipment that is installed in the system. Please note that the export function will fail if there are any errors present in the system.
“Access Point Controller: Check Configuration”, and correct any errors
  To correct synchronization errors run – “Access Point Controller: Check and Update Configuration (SMART HOPPING® Only)”
  If necessary, run – “Access Point Controller: Force Secondary Access Point Controller Configuration Sync”
After all errors are gone, run – “Access Point Controller: Check and Export Access Point Controller Configuration”
An export_YYYYMMDD-HHMMSS.csv file will be created in the “exports” folder that contains software revision information on all the Access Point Controller and Access Points in the system which can be used to identify what hardware is installed in the system.

## Slide 22: Exercise/Exam
Question
Answer

## Slide 23: Question 2
True or False:
The RF performance of the SMART HOPPING® 2.0 Access Point 2.4 GHz allows the Access Point to be placed in the same location as an existing SMART HOPPING® 1.0 Access Point with performance equivalent to the SMART HOPPING® 1.0 system.

## Slide 24: Answer 2
True or False:
The RF performance of the SMART HOPPING® 2.0 Access Point 2.4 GHz allows the Access Point to be placed in the same location as an existing SMART HOPPING® 1.0 Access Point with performance equivalent to the SMART HOPPING® 1.0 system.
Answer 2:
True

## Slide 25: Question 4
True or False:
The SMART HOPPING® 2.0 Access Point 2.4 GHz has been designed to be compatible with SMART HOPPING® 1.0 systems with Access Point Controllers running D.01.01, D.01.02 or D.02.23 software.

## Slide 26: Answer 4
True or False:
The SMART HOPPING® 2.0 Access Point 2.4 GHz has been designed to be compatible with SMART HOPPING® 1.0 systems with Access Point Controllers running D.01.01, D.01.02 or D.02.23 software.
Answer 4:
True

## Slide 27: Question 5
True or False:
Gen 1 and Gen 2 SMART HOPPING® 1.0 2.4 GHz Access Points will not be compatible with future SMART HOPPING® 2.0 wireless clients.

## Slide 28: Answer 5
True or False:
Gen 1 and Gen 2 SMART HOPPING® 1.0 2.4 GHz Access Points will not be compatible with future SMART HOPPING® 2.0 wireless clients.
Answer 5:
True

## Slide 29: Documentation

## Slide 30: Documentation
The SMART HOPPING® documentation portfolio for this release includes the following documents:
453564900981 SMART HOPPING® 2.0 Learning Products Documentation Portfolio *** NEW ***
  453564900901 SMART HOPPING® 2.0 Installation and Configuration Guide *** NEW *** RTX3471 - SMART HOPPING® 2.0 Access Point 2.4GHz Installation Guide *** NEW ***
  453564900971 SMART HOPPING® 2.0 Upgrade Guide *** NEW ***
  453665023231 Accessing SMART HOPPING® Documentation from Philips *** NEW ***
  Existing documents that still apply:
  453564414861 IntelliVue SMART HOPPING® Access Point Controller Installation Guide Edition 2
  453564414891 IntelliVue SMART HOPPING® Synchronization Unit Installation Guide Edition 4
  453564414881 IntelliVue SMART HOPPING® 2.4 GHz Access Point Installation Guide Edition 2

## Slide 31: Products & Ordering
Radio frequency performance – Access Point locations
Internal antenna locations
Mounting alternatives
Technology solutions (VAS)
Ordering

## Slide 32: SMART HOPPING® 2.0 Access Point: Radio frequency performance – Access Point locations
The new SMART HOPPING® 2.0 Access Point can function in existing SMART HOPPING® 1.0 networks today with performance equivalent to the SMART HOPPING® 1.0 system.
Although the physical design and mounting of the SMART HOPPING® 2.0 Access Point are different from the SMART HOPPING® 1.0 Access Point, the radio frequency performance of the SMART HOPPING® 2.0 Access Point allows the Access Point to be placed in the same location as an existing SMART HOPPING® 1.0 Access Point with performance equivalent to the SMART HOPPING® 1.0 system.

## Slide 33: Internal SMART HOPPING® 2.0 antenna locations
The SMART HOPPING® 2.0 Access Point has two internal antennas for the SMART HOPPING® radio.
The flat face of the Access Point must be exposed to the area to be covered for proper radio frequency operation.

## Slide 34: SMART HOPPING® 2.0 Access Point mounting alternatives
Wall mount
Wall mount with cosmetic cover
Below ceiling mount
Below ceiling mount with cosmetic cover
Flush ceiling mount
Technology solutions: Oberon enclosure

## Slide 35: Plenum vs. non-plenum ceiling spaces
Non-plenum ceiling space: Air supply and air return both use ducts.
Plenum ceiling space: Air supply uses ducts, air return does not.
Illustration from: https://www.electricallicenserenewal.com/Electrical-Continuing-Education-Courses/NEC-Content.php?sectionID=57.0
Workspace – patient care areas
Above ceiling/below floor above
Ceiling
Forced Air Supply
NON-PLENUM
Forced Air Return
Workspace – patient care areas
Above ceiling/below floor above
Ceiling
Forced Air Return
Forced Air Supply
PLENUM
Air Support Duct

## Slide 36: SMART HOPPING® 2.0 Access Point mounting alternatives for plenum ceiling space
Wall mount
Wall mount with cosmetic cover
Below ceiling mount
Below ceiling mount with cosmetic cover
Flush ceiling mount
Technology solutions: Oberon enclosure

## Slide 37: Access Point mounting alternatives
SMART HOPPING® 2.0 Access Point basic wall mount
RTX3471
Access Point
(includes mounting bracket)

## Slide 38: Access Point mounting alternatives
SMART HOPPING® 2.0 Access Point wall mount with cosmetic cover
Please find all ordering numbers in Smart Hopping ordering guide:
Cosmetic Cover
RTX3471
Access Point
(includes mounting bracket)
SMART HOPPING 2.0 Ordering guide.pdf

## Slide 39: Access Point mounting alternatives
Ceiling tile
SMART HOPPING® 2.0 Access Point below ceiling mount
Please find all ordering numbers in Smart Hopping ordering guide:
RTX3471
Access Point
(includes mounting bracket)
Mounting rail and associated hardware
SMART HOPPING 2.0 Ordering guide.pdf

## Slide 40: Access Point mounting alternatives
SMART HOPPING® 2.0 Access Point below ceiling mount with cosmetic cover
Please find all ordering numbers in Smart Hopping ordering guide:
Ceiling tile
Mounting rail and associated hardware
RTX3471
Access Point
(includes mounting bracket)
Cosmetic Cover
SMART HOPPING 2.0 Ordering guide.pdf

## Slide 41: Access Point mounting alternatives
SMART HOPPING® 2.0 Access Point flush ceiling mount – exploded view
Please find all ordering numbers in Smart Hopping ordering guide:
Ceiling tile
Mounting rail and associated hardware
Cosmetic Ring
RTX3471
Access Point
(includes mounting bracket)
SMART HOPPING 2.0 Ordering guide.pdf

## Slide 42: Technology solutions (VAS): SMART HOPPING® 2.0 Access Point Oberon enclosure
SMART HOPPING® 2.0 Access Point Oberon enclosure: A new Oberon enclosure and a retrofit door kit for existing installations will also be available.
For more information, please refer to the “Summary List of VAS Products” (no document number) on InCenter.
Door only
SMART HOPPING® 2.0 Access Point in a closed Oberon enclosure
Open Oberon enclosure
Retrofit door kit

## Slide 43: Ordering: Product numbers and options
Description867416 |  | Commercial Product and Option | Notes
SMART HOPPING® 2.0 Access Point 2.4 GHz |  | RTX3471 | Access Point and wall mounting hardware.
SMART HOPPING® 2.0 Installation Material |  | RTX3471 Installation manual | Manuals & guides
SMART HOPPING® 2.0 Frame rail* |  | 94100012 | Metal mounting rail and supporting hardware for either flush ceiling mount or below ceiling mount. For flush ceiling mount must be used with PLAST cosmetic ring.
SMART HOPPING® 2.0 Cosmetic ring |  | 94100013 | PLAST cosmetic ring used in flush ceiling mount. Used with frame rail.
SMART HOPPING® 2.0 Cosmetic cover |  | 94100014 | Cosmetic plastic cover. Can be used with frame rail for below ceiling mount or with the default wall mount to conceal cabling.
*Only available for the US and Canadian markets.

## Slide 44: Ordering: SMART HOPPING® 2.0 Access Point mounting alternatives
 |  | Product number | Description and image | 
Wall mount |  | RTX3471 | SMART HOPPING® 2.0 Access Point 2.4 GHz Includes Access Point and wall mounting hardware | 
For this SMART HOPPING® 2.0 Access Point mounting alternative: |  | Order these SMART HOPPING® 2.0 Installation Material product options: |  | 
Wall mount with cosmetic cover |  | 94100014 | Cosmetic Cover, SMART HOPPING® 2.0 Access Point | 
Flush ceiling mount |  | 94100012* + 94100013 | Mounting Rail, SMART HOPPING® 2.0 Access Point | Cosmetic Ring, SMART HOPPING® 2.0 Access Point
Below ceiling mount |  | 94100012* | Mounting Rail, SMART HOPPING® 2.0 Access Point | 
Below ceiling mount with cosmetic cover |  | 94100012* + 94100014 | Mounting Rail, SMART HOPPING® 2.0 Access Point | Cosmetic Cover, SMART HOPPING® 2.0 Access Point
*Only available for the US and Canadian markets.

## Slide 45: Exercise/Exam
Question
Answer

## Slide 46: Question 6
Which two mounting alternatives CANNOT be used in an air plenum space?
Basic wall mount
Wall mount with a cosmetic cover to cover up the cables
Below ceiling mount
Below ceiling mount with a cosmetic cover to cover up the cables
Flush ceiling mount
Oberon ceiling enclosure (VAS/Technology Solutions product)

## Slide 47: Answer 6
Which two mounting alternatives CANNOT be used in an air plenum space?
Basic wall mount
Wall mount with a cosmetic cover to cover up the cables
Below ceiling mount
Below ceiling mount with a cosmetic cover to cover up the cables
Flush ceiling mount
Oberon ceiling enclosure (VAS/Technology Solutions product)
Answer 6:
a and b - The basic wall mount and the wall mount with the cosmetic cover CANNOT be used in an air plenum space.

## Slide 48: Comparison – Basic Installation
LED and cable connections
Access Point comparison
Ferrite block
LAN connection speed and duplex
LAN connection duplex mismatch

## Slide 49: SMART HOPPING® 2.0 Access Point: LEDs and cable connections
LED 1
Power/Sync
LED 2
Network
LED 3
Radio
LED 4
<Future>
There is no serial port connector.
LAN

## Slide 50: Access Point comparison: Cable connections
LAN
Serial Port
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
There is no serial port connector.
LAN

## Slide 51: Installation differences: Ferrite block
Installation of SMART HOPPING® 1.0 Access Points requires a ferrite block on the LAN cable to reduce electromagnetic interference emissions.
Installation of SMART HOPPING® 2.0 Access Points does not require a ferrite block on the LAN cable to reduce electromagnetic interference emissions.
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
Ferrite block required on LAN cable
Ferrite block not required on LAN cable

## Slide 52: Installation differences: Ferrite block
Installation of SMART HOPPING® 1.0 Access Points requires a ferrite block on the LAN cable to reduce electromagnetic interference emissions.
Installation of SMART HOPPING® 2.0 Access Points does not require a ferrite block on the LAN cable to reduce electromagnetic interference emissions.
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
Ferrite block required on LAN cable
Ferrite block not required on LAN cable
Please note:
If a SMART HOPPING® 1.0 Access Point is replaced by a SMART HOPPING® 2.0 Access Point, the ferrite block
can remain attached to the LAN cable without detrimental impact on the performance of the Access Point.

## Slide 53: Installation differences: LAN connection speed and duplex
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
Ferrite Block no longer required

## Slide 54: Installation differences: LAN connection speed and duplex
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
Ferrite Block no longer required
Shielded cable still required between Switch and Sync Unit

## Slide 55: Installation differences: LAN connection speed and duplex
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
Ferrite Block no longer required
Shielded cable still required between Switch and Sync Unit
SMART HOPPING® 1.0 Access Points are hard coded for 100 Mbps / Full Duplex operation
SMART HOPPING® 2.0 Access Points are hard coded for Auto-negotiation and must operate at 100 Mbps / Full Duplex

## Slide 56: Installation differences: LAN connection speed and duplex
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
Ferrite Block no longer required
Shielded cable still required between Switch and Sync Unit
SMART HOPPING® 1.0 Access Points are hard coded for 100 Mbps / Full Duplex operation
SMART HOPPING® 2.0 Access Points are hard coded for Auto-negotiation and must operate at 100 Mbps / Full Duplex
Installation of SMART HOPPING® 1.0 Access Points requires that the network switchport is hard coded for 100 Mbps / Full Duplex
Installation of SMART HOPPING® 2.0 Access Points requires that the network switchport is hard coded for Auto-negotiation for both speed and duplex
Switchport must be configured for 100 Mbps/Full Duplex
Switchport must be configured for Auto-negotiation for both speed and duplex

## Slide 57: Troubleshooting: LAN connection duplex mismatch
A duplex mismatch occurs when two connected devices are operating in different duplex modes. This may happen if one device is configured for auto-negotiation (the SMART HOPPING® 2.0 Access Point) while the other device (the switch) has a fixed mode of operation (100 Mbps / Full Duplex). This could happen after replacing a SMART HOPPING® 1.0 Access Point with a SMART HOPPING® 2.0 Access Point if the service person forgets to also reconfigure the switchport to auto-negotiate.
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
SMART HOPPING® 1.0 Access Points are hard coded for 100 Mbps / Full Duplex operation
SMART HOPPING® 2.0 Access Points are hard coded for Auto-negotiation and must operate at 100 Mbps / Full Duplex
Switchport must be configured for 100 Mbps/Full Duplex

## Slide 58: Troubleshooting: LAN connection duplex mismatch
A duplex mismatch occurs when two connected devices are operating in different duplex modes. This may happen if one device is configured for auto-negotiation (the SMART HOPPING® 2.0 Access Point) while the other device (the switch) has a fixed mode of operation (100 Mbps / Full Duplex). This could happen after replacing a SMART HOPPING® 1.0 Access Point with a SMART HOPPING® 2.0 Access Point if the service person forgets to also reconfigure the switchport to auto-negotiate.
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
SMART HOPPING® 1.0 Access Points are hard coded for 100 Mbps / Full Duplex operation
SMART HOPPING® 2.0 Access Points are hard coded for Auto-negotiation and must operate at 100 Mbps / Full Duplex
Switchport must be configured for 100 Mbps/Full Duplex
Switchport still configured for 100 Mbps/Full Duplex

## Slide 59: Troubleshooting: LAN connection duplex mismatch
In such situations, the Access Point can detect the speed of operation correctly, but it is unable to correctly detect the duplex mode. As a result, it may default to operating in half-duplex mode.
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
SMART HOPPING® 1.0 Access Points are hard coded for 100 Mbps / Full Duplex operation
Switchport configured for 100 Mbps/Full Duplex
Switchport still configured for 100 Mbps/Full Duplex
SMART HOPPING® 2.0 Access Points are hard coded for Auto-negotiation and may negotiate to 100 Mbps / Half Duplex
Duplex Mismatch

## Slide 60: Installation differences: LAN connection speed and duplex
SMART HOPPING® 1.0 Access Point
SMART HOPPING® 2.0 Access Point
Ferrite Block no longer required
Shielded cable still required between Switch and Sync Unit
SMART HOPPING® 1.0 Access Points are hard coded for 100 Mbps / Full Duplex operation
SMART HOPPING® 2.0 Access Points are hard coded for Auto-negotiation and must operate at 100 Mbps / Full Duplex
Installation of SMART HOPPING® 1.0 Access Points requires that the network switchport is hard coded for 100 Mbps / Full Duplex
Installation of SMART HOPPING® 2.0 Access Points requires that the network switchport is hard coded for Auto-negotiation for both speed and duplex
Switchport configured for 100 Mbps/Full Duplex
Switchport configured for Auto-negotiation for both speed and duplex

## Slide 61: Exercise/Exam
Question 7-8
Answer 7-8

## Slide 62: Question 7
True or False:
The SMART HOPPING® 2.0 Access Point 2.4 GHz requires use of a ferrite block just like the SMART HOPPING® 1.0 Access Points

## Slide 63: Answer 7
True or False:
The SMART HOPPING® 2.0 Access Point 2.4 GHz requires use of a ferrite block just like the SMART HOPPING® 1.0 Access Points
Answer 7:
False

## Slide 64: Question 8
When connecting a SMART HOPPING® 2.0 Access Point 2.4 GHz to the network, for proper operation, what speed and duplex setting must the switch port be configured for?
10 Mbps / Half Duplex
100 Mbps / Full Duplex
Speed and Duplex need to be configured for “Auto-negotiate”

## Slide 65: Answer 8
When connecting a SMART HOPPING® 2.0 Access Point 2.4 GHz to the network, for proper operation, what speed and duplex setting must the switch port be configured for?
10 Mbps / Half Duplex
100 Mbps / Full Duplex
Speed and Duplex need to be configured for “Auto-negotiate”
Answer 8:
c - Speed and Duplex need to be configured for “Auto-negotiate”

## Slide 66: Comparison – Layer 3 Installation
Layer 3 SMART HOPPING® deployments
Access Point web interface

## Slide 67: Installation differences: Layer 3 SMART HOPPING® deployments
In a Layer 3 SMART HOPPING® deployment:
Possible to install on a Customer Supplied Network (not on a Philips Supplied Network)
Access Point Controller and Wireless Clients are on the same subnet, and Access Points are on different subnets
Access Point Controller provide the DHCP service to the Wireless Clients
The hospital provides the DHCP service (using Option 43) to the Access Points
Access Point Controller and Access Points discover each other using multicast
The Access Point Controller VLAN must be configured to use IGMP (Internet Group Management Protocol) version 3*
*Reference SB86202793A: 865346 Access Point Controller SMART HOPPING® Layer 3 Deployments – Troubleshooting Topic: IGMP Version
Symptoms:
Access Point Controller VLAN: When an Access Point Controller is added to the network, or if the Access Point Controller is rebooted, there may be a change in which Access Point Controller is operating as the Primary Access Point Controller.
Access Point VLANs: Access Points will power on and operate for 1-2 minutes and then will reboot.
SMART HOPPING® 2.0 Access Points used in a Layer 3 SMART HOPPING® deployment
Access Point VLANs may be configured to use IGMP version 1 (required for mixed SMART HOPPING® 1.0 and SMART HOPPING® 2.0 systems) or IGMP version 2 (if all the Access Points in the system are SMART HOPPING® 2.0)
SMART HOPPING® 1.0 Access Points used in a Layer 3 SMART HOPPING® deployment
Access Point VLANs must be configured to use IGMP version 1*

## Slide 68: Installation differences: Layer 3 SMART HOPPING® deployments
Configuring Multicast Addresses for Layer 3 operation
SMART HOPPING® 1.0 Access Points
From factory, the Access Points use the Layer 3 default multicast addresses
  Primary Access Point Controller: 239.255.254.1
  Secondary Access Point Controller: 239.255.254.2
DHCP Option 43
Manual Entry (through serial port on Access Point)
SMART HOPPING® 2.0 Access Points
From factory, the Access Points use the Layer 3 default multicast addresses
  Primary Access Point Controller: 239.255.254.1
  Secondary Access Point Controller: 239.255.254.2
DHCP Option 43
Manual Entry (through Access Point web interface)

## Slide 69: Installation differences: Layer 3 SMART HOPPING® deployments
Configuring Multicast Addresses for Layer 3 Operation
SMART HOPPING® 1.0 Access Points
From factory, the Access Points use the Layer 3 default multicast addresses
  Primary Access Point Controller: 239.255.254.1
  Secondary Access Point Controller: 239.255.254.2
DHCP Option 43
Manual Entry (through serial port on Access Point)
SMART HOPPING® 2.0 Access Points
From factory, the Access Points use the Layer 3 default multicast addresses
  Primary Access Point Controller: 239.255.254.1
  Secondary Access Point Controller: 239.255.254.2
DHCP Option 43
Manual Entry (through Access Point web interface)
DHCP Option 43 is the preferred method to assign the multicast addresses
DHCP Option 43 is still the preferred method to assign the multicast addresses

## Slide 70: Installation differences: Layer 3 SMART HOPPING® deployments
Configuring Multicast Addresses for Layer 3 Operation
SMART HOPPING® 1.0 Access Points
From factory, the Access Points use the Layer 3 default multicast addresses
  Primary Access Point Controller: 239.255.254.1
  Secondary Access Point Controller: 239.255.254.2
DHCP Option 43
Manual Entry (through serial port on Access Point)
SMART HOPPING® 2.0 Access Points
From factory, the Access Points use the Layer 3 default multicast addresses
  Primary Access Point Controller: 239.255.254.1
  Secondary Access Point Controller: 239.255.254.2
DHCP Option 43
Manual Entry (through Access Point web interface)
DHCP Option 43 is the preferred method to assign the multicast addresses
DHCP Option 43 is still the preferred method to assign the multicast addresses
If necessary, the multicast addresses can be configured via a new Access Point web browser page

## Slide 71: Installation differences: Layer 3 SMART HOPPING® deployments
Configuring Multicast Addresses for Layer 3 Operation
Manual Entry (through Access Point web page)
  Browse to the Access Point’s IP address using port 8443: https://172.31.2.131:8443
  (These screens shots are from Chrome.) Since the Access Point uses a self-signed certificate, you will receive a security warning, select “Advanced” and then “Proceed to 172.31.2.131 (unsafe)”

## Slide 72: Installation differences: Layer 3 SMART HOPPING® deployments
Configuring Multicast Addresses for Layer 3 Operation
Manual Entry (through Access Point web interface)
  When prompted, enter in the Username and Password
Please Note: There is no timeout feature for the web interface. Be certain to close the web interface after completing the desired service action.

## Slide 73: Installation differences: Layer 3 SMART HOPPING® deployments
Configuring Multicast Addresses for Layer 3 Operation
Manual Entry (through Access Point web page)
  Select the “Multicast” tab

## Slide 74: Installation differences: Layer 3 SMART HOPPING® deployments
Configuring Multicast Addresses for Layer 3 Operation
Manual Entry (through Access Point web page)
  Select the “Multicast” tab
  Modify the multicast addresses as necessary, and select “Safe”.
Please Note: There is no timeout feature for the web interface. Be certain to close the web interface after completing the desired service action.

## Slide 75: Installation differences: Access Point web interface password
Configuring Access Point Web Interface Password
Must be at least 14 and at most 32 characters, with at least 1 upper case, 1 lower case, 1 digit and 1 special character.
Select “Change password” tab
Enter current password
Enter new password
Enter new password again to confirm
Select “Change password”
This is done on each Access Point individually
If the password is forgotten, the only thing that can be done is to reload the software which resets it back to the factory default value.

## Slide 76: Access Point web interface: Other information available – Status Tab
Serial Number!!
Service Number!!
Software
Revision in
new format

## Slide 77: Access Point web interface: Other information available – Syslog
Syslog Tab
Last 100 entries
Syslog (all) Tab
Last 1,000,000 entries

## Slide 78: Access Point web interface: Other information available – Syslog
Syslog Tab
Last 100 entries
Syslog (all) Tab
Last 1,000,000 entries
Syslog is used primarily by R&D for troubleshooting

## Slide 79: Access Point web interface: Other information available – http error log
HTTP error log
This log is used primarily by R&D for troubleshooting.

## Slide 80: Access Point web interface: Other information available – HTTP access log
HTTP access log
This log is used primarily by R&D for troubleshooting.

## Slide 81: Exercise/Exam
Question
Answer

## Slide 82: Question 9
For a Layer 3 SMART HOPPING® deployment using SMART HOPPING® 2.0 Access Points, if DHCP Option 43 is not used, and the multicast addresses need to be configured manually, what interface is used?
The serial console port on the Access Point.
The new Access Point web browser page.

## Slide 83: Answer 9
For a Layer 3 SMART HOPPING® deployment using SMART HOPPING® 2.0 Access Points, if DHCP Option 43 is not used, and the multicast addresses need to be configured manually, what interface is used?
The serial console port on the Access Point.
The new Access Point web browser page.
Answer 9:
b - The new Access Point web browser page.

## Slide 84: Troubleshooting
LEDs troubleshooting table
LAN connection duplex mismatch
Speed and duplex problems with Service PC Connection

## Slide 85: SMART HOPPING® 2.0 Access Point: LEDs troubleshooting table (1 of 2)
LED 1
Power / Sync
LED 2
Network
LED 3
Radio
LED 4
<Future>
 | LED 1 Power / Sync | LED 2 Network | LED 3 Radio | LED4 Future | Troubleshooting Information
Normal Operation: Access Point only | Green | Flashing Green | Flashing Green | Off | Power/Sync, Network, and Radio are working properly.
Normal Operation: Access Point and Remote Antennas | Green | Flashing Green | Flashing Amber | Off | Power/Sync, Network and Radio, are working properly.
Action Required | Off | Off | Off | Off | The Access Point is not receiving power. Confirm that the POE switch has power to the Access Point port enabled. Check connectivity from the Access Point, through the Sync Unit to the POE switch.
Action Required | Green | Flashing Green | Flashing Red | Off | Power/Sync and Network are working properly. However, there is an issue with the radio. Confirm proper operation of the Access Point rebooting the Access Point. Replace Access Point if after the reboot the Radio LED does not flash green (normal operation for an Access Point only).

## Slide 86: SMART HOPPING® 2.0 Access Point: LEDs troubleshooting table (2 of 2)
 | LED 1 Power / Sync | LED 2 Network | LED 3 Radio | LED4 Future | Troubleshooting Information
Action Required | Flashing Red | Flashing Green | Flashing Green | Off | The Access Point has lost local synchronization (no synchronization pulses). Check connection to and functionality of the directly connected Sync Unit.
Action Required | Flashing Green | Flashing Green | Flashing Green | Off | The Access Point has detected loss of remote synchronization. Check connection to and functionality of the Sync Units connected further upstream of the directly connected Sync Unit.
Action Required | Amber | Amber | Amber | Off | The Access Point is not registered to any Access Point Controller. Check network connectivity from the Access Point to the Access Point Controller. Basic SMART HOPPING® network discovery uses broadcast for Layer 2 deployments and multicast for Layer 3 deployments.
Action Required (if LED state is persistent) | Red | Off | Off | Off | If the Access Point is in this state for more than 5 seconds, this indicates that the Access Point has power but has a hardware fault. Replace the Access Point.
Action Required | Flashing Red | Flashing Red | Flashing Red | Off | Hardware POST (Power On Self Test) failure (there is an issue with one or more of the following components: DRAM, Flash Memory, CPU, Radio, LAN Interface). Replace the Access Point.
Device Boot in Progress | Amber | Amber | Amber | Amber | Wait for boot process to complete.
Service Event in Progress | Blue | Off | Off | Off | Service event in progress. Access Point is receiving new firmware. After the download is complete, access points will be restarted to accept the new image. This is managed by the SMART HOPPING® Infrastructure Support Tool (Upgrader Tool).
LED 1
Power / Sync
LED 2
Network
LED 3
Radio
LED 4
<Future>

## Slide 87: Troubleshooting: LAN connection duplex mismatch
When one device is operating in full duplex while the other one operates in half duplex, the connection works reliably only at a very low throughput. A full duplex device (the switch in this situation) may transmit data while it is receiving. However, if the half duplex device (the Access Point) receives data while it is sending, it senses a collision and aborts transmission and then attempts to resend the frame. The full-duplex device (the switch) will report frame check sequence (FCS) errors on the aborted transmissions.
Depending on timing, the half-duplex device (the Access Point) may sense a late collision, which it will interpret as a hard error rather than a normal consequence of CSMA/CD and may not attempt to resend the frame. The full-duplex device (the switch) does not detect any collision and assumes the frame was received without error (lost data).
Unfortunately, the Access Point does not report Ethernet performance statistics. FCS errors reported by the switch would be an indication that a duplex mismatch is present.
SMART HOPPING® 2.0 Access Point
Switchport still configured for 100 Mbps/Full Duplex
SMART HOPPING® 2.0 Access Points are hard coded for Auto-negotiation and may negotiate to 100 Mbps / Half Duplex
Duplex Mismatch
Symptoms of duplex mismatch: The switchport will report Frame Check Sequence (FCS) errors.

## Slide 88: Troubleshooting: LAN connection duplex mismatch
Cisco switch commands: show interface status
Shows how the switchports are configured and how they are operating
Active connection configured for and operating at 100Mbps/Full Duplex
Active connection configured for auto-negotiate and operating at 100Mbps/Full Duplex
No devices connected
No devices connected

## Slide 89: Troubleshooting: LAN connection duplex mismatch
Cisco switch commands: show interface fa0/## controller
Shows switchport statistics, including FCS errors
duplex mismatch

## Slide 90: Troubleshooting speed and duplex problems with Service PC Connection
To check actual operation of the NIC in a PC, go to the network adapter and get the NIC product number (e.g. “I219-LM”).

## Slide 91: Troubleshooting speed and duplex problems with Service PC Connection
Go to Event Viewer, select “Windows Logs”, then double click on “System”.

## Slide 92: Troubleshooting speed and duplex problems with Service PC Connection
Go to Event Viewer, select “Windows Logs”, then double click on “System”
On the right, select “Find”, and then enter the product number of the NIC – e.g. “I219-LM” and select “Find Next”. This will take you to the next event for the NIC.

## Slide 93: Troubleshooting speed and duplex problems with Service PC Connection
In the event it will provide information on the name of the source of the event – this is what you want to filter on.
e.g. Source = “e1dexpress”

## Slide 94: Troubleshooting speed and duplex problems with Service PC Connection
To check actual operation of the NIC in a PC, go to Event Viewer
Select “Filter Current Log”, and then select the NIC from the “Event sources” list.

## Slide 95: Troubleshooting speed and duplex problems with Service PC Connection
Now you have the list of events logged by the NIC.
Events like disconnecting from the network, and what speed and duplex the NIC is using will be logged.
In this example, the NIC is using 100Mbps – Half Duplex which is a problem.

## Slide 96: Test & Inspection

## Slide 97: SMART HOPPING® 2.0 Access Point: Test and inspection
At the top level, the tests required for the various service events will remain the same as those for the SMART HOPPING® 1.0 Access Points and Remote Antennas:

## Slide 98: SMART HOPPING® 2.0 Access Point: Test and inspection
The “AP Power On” test will be modified to add the SMART HOPPING® 2.0 Access Point since the LEDs are different:
All other tests (Access Point Visual, Access Point Performance, Access Point Revision Check, Coverage Area Verification) will be the same as for the SMART HOPPING® 1.0 Access Points.
AP Power On | With power connected to each active Network device, observe that all lights visible on the front panel are in proper status and that no error conditions are shown. Note that for 1.4 GHz Core AP’s and 2.4 GHz AP’s, you can view the Power, Network and Radio LEDs from the AP Status page in the APC web interface. RTX3471 Verify that Power/Sync LED on Core AP are lit Solid GREEN. Verify that Network LED on Core AP is lit Blinking GREEN. 989803171211, 989803171221 and 862228 Verify the Link and Power/Sync LEDs on AP are lit Solid GREEN. Verify that Activity LED is Blinking YELLOW. Verify that Radio and Network LEDs on Core AP are lit Blinking GREEN. 862113 and 862232 Verify the FDX, 100M, Link and Power/Sync LEDs are lit Solid GREEN. Verify the Activity, Radio and Network LEDs are lit Blinking GREEN. | Devices power up into expected status; no error indications are shown | PO:P or PO:F Where: P=Pass F=Fail